## Slide 1: JUNOS Automation Project Walk Trough
Levent Ogut (logut@juniper.net)
February 2014

## Slide 2: Agenda
  Requirement Gathering
  Review of Requirements
  Very High Level Pseudo Code
  Development Environment
  Script Documentation
  Debug / Trace
  Local Development Options
  Local Development vis RPC output
  Simple Juise Demo
  Juise Debugging Demo
  Juise Profiling Demo
  Slacproc Syntax Checking
  Testing
  Versioning (Local) - Git Demo
  Py-junos-eznc Demo
  Resources

## Slide 3: Customer’s Requirements – Fastweb ITaly
  CGNAT DETNAT Configuration Tracker
  XML output of the NAT Rule and NAT Pool configuration when there is a configuration change on [services] stanza
  Filename should in the following format:
    <router-name>_<YYYYMMDD>_<HHMMSS>_<counter>.xml
    <router-name> = network element unique name
    <YYYYMMDD> = validity configuration starting date (ex: “20130917” for the day 2013-09- 17)
    <HHMMSS> = validity configuration starting time (ex: “173404” for the time 17 h 34 m 04 s) <counter>=progressiveindex (ex:“7”)
    e.g. milano_20130917_173404_7.xml
  Transfer of the file to a remote server via SFTP with *.tmp extension
  Rename the remote file from *.tmp to *.xml (so that server side knows transfer is completed)

## Slide 4: Customer’s Requirements – Fastweb ITaly
  <juniper-configuration>
  <pools>
  <pool>
  <public>
  <ip_min>32.32.32.1</ip_min>
  <ip_max>32.32.32.254</ip_max>
  </public>
  <private>
  <network>10.1.0.0/16</network>
  </private>
  <block_size>50</block_size>
  <port_range_per_pu_ip>50</port_range_per_pu_ip>
  </pool>
  </pools>
  </juniper-configuration>

## Slide 5: What can we do and what we can’t do
  After a research I found:
    SFTP is not supported on customer’s JUNOS version (11.4)
      SCP is recommended to customer
    We can not rename the file we transferred
      Instead, an empty file will be transferred to server after SUCCESSFUL transfer of the original XML file. So server side script need to look to this file to determine transfer success.
  All agreed with customer, now we can develop!

## Slide 6: Very High Level PseUdoCODe
  Check if we are running in master RE
    if not, then do nothing i.e. exit silently
  Check if this is a “commit check” operation
    if yes, then do nothing i.e. exit silently
  Check if there is change in [services] stanza continue
    if not, then do nothing i.e. exit silently
  Traverse all NAT Rules to gather following:
    Traverse each term for “source-address” and “source-address-range”
    Translated [source-pool] name
      For each pool gather:
        Address and address-range
  Put all information into predetermined format and write to a file
  Transfer the file
    If transfer is successful, upload a *.CMP empty file to server as well
    If transfer fails then do not delete the CMP file in local

## Slide 7: Development Environment
  Any editor that you are comfortable with
    Sublime Text 2 / 3
    Text Mate
    Vim
    emacs
    MacVim
    Notepad++
    Jedit
    Etc.
  Juise
  import "../import/junos.xsl";
  SCP / CyberDuck / WinSCP etc. for transferring files

## Slide 8: Directory Hierarchy - LOCAL
  PIDxxx_Customer_Project_Name/
    Customer.Provided/
      Customer docs etc
    dev/
      import/
        junos.xsl
      commit/op/event/
        SCRIPT_name.slax
        test.slax

## Slide 9: Directory Hierarchy - ROUTER
  --- JUNOS 12.3R5.7 built 2013-12-18 01:32:46 UTC
  logut@flint> start shell
  % cd /var/db/scripts/
  % ls -al
  total 64
  drwxr-xr-x 7 root wheel 512 Feb 5 12:11 .
  drwxr-xr-x 15 root wheel 1024 Feb 5 12:49 ..
  drwxrws--- 2 root wheel 512 Feb 5 12:11 commit
  drwxrws--- 2 root wheel 18944 Feb 5 12:11 event
  lrwxr-xr-x 1 root wheel 27 Feb 5 12:11 import -> /usr/libdata/cscript/import
  drwxrws--x 2 root wheel 512 Oct 8 2011 lib
  drwxrws--- 2 root wheel 512 Feb 5 12:11 op
  drwxrws--- 2 root wheel 512 Feb 4 14:27 snmp
  %

## Slide 10: Screen Capture from Editor

## Slide 11: Script Documentation
  /*
  * Filename : <script_name>.slax
  * Author : <Author Name> / <author_email>
  * version : 0.1
  * Platform : xx
  * Release : Junos 11.4+
  *
  * Copyright 2014 Juniper Networks. All rights reserved.
  */
  /*
  ### Description
  ### Installation
  xxxx
  xxxxx

## Slide 12: Script Documentation
  ### Configuration
  [ system scripts ]
  commit {
  file <script_name>.slax;
  }
  ### Enabling Traceoptions
  [ system scripts ]
  commit {
  traceoptions {
  file commit.trace size 1m world-readable;
  }
  }

## Slide 13: Script Documentation
  ### Caveats and Notes
  ### Change Log
  0.1 initial script
  0.2 New feature: script to communicate with other scripts via Morse code
  1.0 release
  1.1 bug fix: script shouldn’t trigger “blow up” datacenter, unless...
  ### Sample Output
  <?xml version="1.0"?>
  <juniper-configuration>
  <pools>
  <pool>
  <public>
  <ip_min>80.2.0.161</ip_min>
  <ip_max>80.2.0.166</ip_max>
  </public>

## Slide 14: Script Documentation
  ### Parameters / Variables
  ## Set on top of the script
  #### Where to save local file
  var $path = "/var/tmp/";
  #### Local filename extension
  var $extension = ".xml";
  var $extension_cmp = ".cmp";
  #### Remote Server Parameters 172.29.65.139
  var $scp_user = 'tsd0scp';
  var $scp_host = '172.29.64.34';
  var $scp_dst_dir = '';
  END OF DOCUMENTATION
  */

## Slide 15: Script Documentation
  Documentation is crucial
  Someone else might need to work on that script after you.
  And you would want to avoid customer / calls for small installation/configuration/parameter change issues.

## Slide 16: Development
  Templates I think I need (some of them thought throughout development):
  # Delete file
  template file_delete ($filename)
  # Transfer file
  template tx_file ($file_path, $filename, $host, $user, $dst_path)
  # convert 1.1.1.0/24 to 1.1.1.1 1.1.1.254
  template prefix2min_max ($address)
  # convert IP to decimal for calculations
  template ip2decimal($ip)
  # convert 1.1.1.1 1.1.1.254 to 1.1.1.0/24
  template low_high2prefix ($low="",$high="”)
  # generate filename using host / datetime / sequence number / extension
  template generate_filename ()
  # write a file to local
  template write2file ($filename, $content)
  # Check if the RE that script is running is master
  template is_master ()

## Slide 17: Development
  With the templates above now the main code is clean and more understandable

## Slide 18: Development
  var $re_status = { call is_master(); }
  /* check if it is commit check, if it is exit , we are only interested on actual commit operations */
  if ($junos-context/commit-context/commit-check) {
  expr jcs:trace( $script, " This is a commit check not an actual commit, not executing rest");
  }
  else if ($re_status != 1) {
  expr jcs:trace( $script, " This RE is not the master, script only runs on master RE, not executing rest for backup RE");
  }

## Slide 19: Development
  else {
  var $result_config_services = services;
  /* check of the services configuration has been changed or not */
  if( $result_config_services[@junos:changed=="changed"] ) {
  expr jcs:trace( $script, " Configuration change for <services> stanza detected, generating XML structure and transfering file");

## Slide 20: Development
  var $juniper_configuration = {
  <juniper-configuration>{
  <pools> {
  for-each ($result_config_services/nat/rule) {
  for-each (./term) {
  <pool> {
  /*
  NAT source definitions and calculations
  Private Block format:
  <private>
  <network>10.1.0.0/16</network>
  </private>
  */
  var $private_prefix = ./from/source-address/name;
  var $private_low = ./from/source-address-range/low;
  var $private_high = ./from/source-address-range/high;
  var $private_actual := {

## Slide 21: Development
  Error Handling
  template tx_file ($file_path, $filename, $host, $user, $dst_path) {
  var $file-copy-rpc =
  <file-copy> {
  <source> $file_path _ $filename _ $extension;
  <destination> "scp://" _ $user _ "@" _ $host _ ":" _ $dst_path;;
  }
  var $results = jcs:execute( $connection, $file-copy-rpc );
  /* Report any errors or success */
  if( $results/..//xnm:error ) {
  for-each( $results/..//xnm:error ) {
  expr jcs:syslog( "external.error", "File Copy Error: ", message );
  }
  expr jcs:trace( $script, " tx_file : there was a proble with file transfer : ", $results);
  }
  else {
  var $file-cmp-copy-rpc =
  <file-copy> {
  <source> $file_path _ $filename _ $extension_cmp;
  <destination> "scp://" _ $user _ "@" _ $host _ ":" _ $dst_path;;
  }
  var $results_cmp = jcs:execute( $connection, $file-cmp-copy-rpc );
  expr jcs:syslog( "external.info", "services XML structure sucessfully transfered." );
  expr jcs:trace( $script, " tx_file : file transfer successful!");
  /* when file transfer is successful, delete the CMP file on local,meaning file tx'd sucessfully, if there is errors we don't delete the files */
  call file_delete ($filename=$path _ $filename _ $extension_cmp);
  }
  }

## Slide 22: Debug / TRACE
  Always use jcs:trace()
  In script:
  if( $result_config_services[@junos:changed=="changed"] ) {
  expr jcs:trace( $script, " Configuration change for <services> stanza detected, generating XML structure and transferring file");
  /* Generate the XML output */
  In Config:
  [edit system scripts commit]
  logut@death# show
  traceoptions {
  file mycommitScript.trace world-readable;
  }
  file cgnat_cfg_tracker_comm.slax;
  Log:
  Feb 7 11:28:05 running commit script 'cgnat_cfg_tracker_comm.slax'
  Feb 7 11:28:05 cgnat_cfg_tracker_comm.slax No configuration change for <services> stanza detected, skipping generating XML structure
  Feb 7 11:28:05 processing commit script 'cgnat_cfg_tracker_comm.slax'

## Slide 23: OP / EVENT / COMMIT Script
  I write every script as an op script initially.
  This allows me to run/debug with ease.
  After all parsing modification is complete I convert it to event/commit where needed.

## Slide 24: Local Development
  If you are going to work on parsing an RPC reply and modify it / display it differently / log it then you can also work on your local machine by getting the RPC reply from a router and providing that on to the script.

## Slide 25: Local Development
  var $result_config_services := {
  <nat> {
  <pool> {
  <name>"test_pool1";
  <address> {
  <name>"80.1.0.0/16";
  }
  <port> {
  <range> {
  <low>"1025";
  <high>"1074";
  }
  <deterministic-port-block-allocation>{
  <block-size>"50";
  }
  }
  }
  <pool> {
  <name>"test_pool2";
  <address> {
  <name>"80.2.0.0/16";
  }
  <port> {
  <range> {
  <low>"1025";
  <high>"1074";
  }
  <deterministic-port-block-allocation>{
  <block-size>"50";
  }
  }
  }

## Slide 26: Local Development
  logut-mba13:zArchive logut$ juise cgnat_cfg_tracker_prototype.slax
  logut-mba13:zArchive logut$ cat /var/tmp/proto_test.xml
  <?xml version="1.0"?>
  <juniper-configuration>
  <pools>
  <pool>
  <public>
  <ip_min>80.1.0.1</ip_min>
  <ip_max>80.1.255.254</ip_max>
  </public>
  <private>
  <network>10.1.0.0/16</network>
  </private>
  <block_size>50</block_size>
  <port_range_per_pu_ip>50</port_range_per_pu_ip>
  </pool>
  <pool>
  <public>
  <ip_min>80.2.0.1</ip_min>
  <ip_max>80.2.255.254</ip_max>
  </public>
  <private>
  <network>10.2.0.0/16</network>
  </private>
  <block_size>50</block_size>
  <port_range_per_pu_ip>50</port_range_per_pu_ip>
  </pool>
  </pools>
  </juniper-configuration>
  logut-mba13:zArchive logut$

## Slide 27: Execution via Juise
  version 1.0;
  ns junos = "http://xml.juniper.net/junos/*/junos";
  ns xnm = "http://xml.juniper.net/xnm/1.1/xnm";
  ns jcs = "http://xml.juniper.net/junos/commit-scripts/1.0";
  import "../import/junos.xsl";
  match / {
  var $rpc_show_version = <get-software-information>;
  var $results_show_version = jcs:invoke($rpc_show_version);
  expr "hostname : " _ $results_show_version/host-name _ '\n';
  expr "model : " _ $results_show_version/product-model _ '\n';
  for-each ($results_show_version/package-information) {
  expr ./comment _ '\n';
  }
  }

## Slide 28: Execution via Juise
  logut-mba13:op logut$ juise logut@death.jtac-emea.jnpr.net show_version.slax
  logut@death.jtac-emea.jnpr.net's password:
  <?xml version="1.0" standalone="yes"?>
  hostname : death
  model : m120
  JUNOS Base OS boot [10.4S7.1]
  JUNOS Base OS Software Suite [10.4S7.1]
  JUNOS Kernel Software Suite [10.4S7.1]
  JUNOS Crypto Software Suite [10.4S7.1]
  JUNOS Packet Forwarding Engine Support (M/T Common) [10.4S7.1]
  JUNOS Packet Forwarding Engine Support (M120) [10.4S7.1]
  JUNOS Online Documentation [10.4S7.1]
  JUNOS Voice Services Container package [10.4S7.1]
  JUNOS Border Gateway Function package [10.4S7.1]
  JUNOS Services AACL Container package [10.4S7.1]
  JUNOS Services LL-PDF Container package [10.4S7.1]
  JUNOS Services PTSP Container package [10.4S7.1]
  JUNOS Services Stateful Firewall [10.4S7.1]
  JUNOS Services NAT [10.4S7.1]
  JUNOS Services Application Level Gateways [10.4S7.1]
  JUNOS Services Captive Portal and Content Delivery Container package [10.4S7.1]
  JUNOS Services RPM [10.4S7.1]
  JUNOS AppId Services [10.4S7.1]
  JUNOS IDP Services [10.4S7.1]
  JUNOS Runtime Software Suite [10.4S7.1]
  JUNOS Routing Software Suite [10.4S7.1]
  JUNOS AIS Script Suite [3.7R3.0]

## Slide 29: Local Development – Juise - Debuging
  logut-mba13:dev logut$ juise --debug test.slax
  sdb: The SLAX Debugger (version 0.14.4)
  Type 'help' for help
  (sdb) next
  junos.xsl:23: <xsl:param name="localtime-iso"/>
  (sdb) next
  junos.xsl:25: <xsl:param name="script"/>
  (sdb) next
  test.slax:15: var $debug=1;
  (sdb) print $debug
  [number] 1.000000
  …………(cut for brevity)
  (sdb) next
  test.slax:19: var $hello = "script is running";
  (sdb) next
  test.slax:20: <output> $hello;
  (sdb) print $hello
  [string] "script is running"
  (sdb)

## Slide 30: Local Development – Juise - Callflow
  logut-mba13:dev logut$ juise --debug cgnat_cfg_tracker_prototype.slax
  sdb: The SLAX Debugger (version 0.14.4)
  Type 'help' for help
  (sdb) callflow
  Enabling callflow
  (sdb) run
  callflow: 0: enter <xsl:template> in match / at cgnat_cfg_tracker_prototype.slax:102
  callflow: 1: enter <nat> at cgnat_cfg_tracker_prototype.slax:119
  callflow: 1: exit <nat> at cgnat_cfg_tracker_prototype.slax:119
  callflow: 1: enter <juniper-configuration> at cgnat_cfg_tracker_prototype.slax:195
  callflow: 2: enter <xsl:for-each> at cgnat_cfg_tracker_prototype.slax:198
  callflow: 3: enter <pool> at cgnat_cfg_tracker_prototype.slax:199
  callflow: 4: enter <xsl:if> at cgnat_cfg_tracker_prototype.slax:212
  callflow: 5: enter <prefix> at cgnat_cfg_tracker_prototype.slax:213
  callflow: 5: exit <prefix> at cgnat_cfg_tracker_prototype.slax:213
  callflow: 4: exit <xsl:if> at cgnat_cfg_tracker_prototype.slax:212
  callflow: 4: enter <xsl:if> at cgnat_cfg_tracker_prototype.slax:235
  callflow: 5: enter <xsl:variable> at cgnat_cfg_tracker_prototype.slax:240
  callflow: 6: enter <xsl:call-template> at cgnat_cfg_tracker_prototype.slax:240
  callflow: 7: enter <xsl:template> in template prefix2min_max at cgnat_cfg_tracker_prototype.slax:323

## Slide 31: Local Development – Juise - Profiling
  logut-mba13:zArchive logut$ juise -d cgnat_cfg_tracker_prototype.slax
  sdb: The SLAX Debugger (version 0.14.4)
  Type 'help' for help
  (sdb) run
  Script exited normally.
  (sdb) profile report brief
  Line Hits User U/Hit System S/Hit Source
  90 1 3 3.00 2 2.00 var $debug = 1;
  92 1 2 2.00 1 1.00 var $path = "/var/tmp/";
  93 1 2 2.00 1 1.00 var $extension = ".tmp";
  96 1 2 2.00 1 1.00 var $scp_user = 'slax';
  97 1 6 6.00 5 5.00 var $scp_host = '172.29.65.139';
  98 1 2 2.00 1 1.00 var $scp_dst_dir = '';
  102 2 4 2.00 3 1.50 match / {
  118 2 21 10.50 5 2.50 var $result_config_services := {
  119 1 5 5.00 1 1.00 <nat> {
  120 1 2 2.00 1 1.00 <pool> {
  121 1 3 3.00 1 1.00 <name>"test_pool1”;

## Slide 32: Local Development – Juise - Profiling
  Line—Line number in the source file.
  Hits—Number of times this line was executed.
  User—Number of microseconds of "user" time spent processing this line.
  U/Hit—Average number of microseconds of "user" time per hit.
  System—Number of microseconds of "system" time spent processing this line.
  S/Hit—Average number of microseconds of "system" time per hit.

## Slide 33: SLAXPRoC – Local Syntax Checking
  logut-mba13:dev logut$ slaxproc --check cgnat_cfg_tracker_comm.slax
  script check succeeds
  logut-mba13:dev logut$

## Slide 34: Testing
  Testing is an important part, this is a product of CS/AS/PS/What’s your name!
  Testing depends type of script, make sure errors are handled.
  Obviously develop & test on the target JUNOS and architecture / platform.
  Dual-RE tests are important for commit scripts
  Changing configurations is not trivial task, make sure it is clean.

## Slide 35: General Rules
  DRY ( Don’t Repeat Yourself)
  While developing customer scripts think about the future, if a part of the script is reusable, make it as a template ().
  As AS/JTAC/PS/JNPR we develop lots of scripts but collaboration on this regard is poor IMHO.
  Ask, everyone in JNPR is willing to help.

## Slide 36: Workflow – GIT – Create Repository
  logut-mba13:tmp logut$ mkdir automation_demo
  logut-mba13:tmp logut$ cd automation_demo/
  logut-mba13:automation_demo logut$ ll
  Initializing GIT Repo
  logut-mba13:automation_demo logut$ git init
  Initialized empty Git repository in /Users/logut/tmp/automation_demo/.git/
  Creating Our File
  logut-mba13:automation_demo logut$ touch test.slax
  logut-mba13:automation_demo logut$ echo "deneme" > test.slax

## Slide 37: Workflow – GIT – STATUS – Adding a FILE
  After Our Changes Looking to Git
  logut-mba13:automation_demo logut$ git status
  # On branch master
  #
  # Initial commit
  #
  # Untracked files:
  # (use "git add <file>..." to include in what will be committed)
  #
  # test.slax
  nothing added to commit but untracked files present (use "git add" to track)
  Adding our new file to Git for tracking
  logut-mba13:automation_demo logut$ git add test.slax

## Slide 38: Workflow – GIT – STATUS and first commit
  logut-mba13:automation_demo logut$ git status
  # On branch master
  #
  # Initial commit
  #
  # Changes to be committed:
  # (use "git rm --cached <file>..." to unstage)
  #
  # new file: test.slax
  #
  logut-mba13:automation_demo logut$ git commit -m "initial commit"
  [master (root-commit) 68a1b15] initial commit
  1 file changed, 1 insertion(+)
  create mode 100644 test.slax

## Slide 39: Workflow – GIT – Second change and commit
  logut-mba13:automation_demo logut$ echo "second line change" >> test.slax
  logut-mba13:automation_demo logut$ git add test.slax
  logut-mba13:automation_demo logut$ git commit -m "my second commit"
  [master 5f4f038] my second commit
  1 file changed, 1 insertion(+)

## Slide 40: Workflow – GIT - LOG
  logut-mba13:dev logut$ git log
  commit 97660ab5f910940d94f2ef6efd7713024b2d82ba
  Author: Levent Ogut <logut@juniper.net>
  Date: Wed Feb 5 01:06:50 2014 +0200
  public/private low/high & prefix input support
  commit c52c302215800c03ec1ca2be4a8563408810cb76
  Author: Levent Ogut <logut@juniper.net>
  Date: Fri Jan 31 12:50:12 2014 +0200
  fix for backup RE error, preventing the commit
  commit 496a2b885ecde9df2114940364ffe46296fc766f
  Author: Levent Ogut <logut@juniper.net>
  Date: Thu Jan 9 13:15:51 2014 +0200
  archive update
  commit 5619c6cfb331ac2ebbe1c755440716d0e25394eb
  Author: Levent Ogut <logut@juniper.net>
  Date: Wed Dec 18 18:28:44 2013 +0200
  file tx changes and error handling
  commit 10d67fb614f9162daa2c158b91baf8b3cc3091cb
  Author: Levent Ogut <logut@juniper.net>
  Date: Wed Dec 18 17:24:20 2013 +0200
  f
  commit 8da4013dd20c6d8d749eaefe46614f2d4c7bbad3
  Author: Levent Ogut <logut@juniper.net>
  Date: Wed Dec 18 17:11:18 2013 +0200
  change of fle transfer
  commit 85e7be3009bb7155c46e0fde0fb3e6148b7d98a3
  Author: Levent Ogut <logut@juniper.net>
  Date: Wed Dec 18 16:06:17 2013 +0200

## Slide 41: Workflow – GIT - DIff
  logut-mba13:dev logut$ git status
  # On branch master
  # Changes not staged for commit:
  # (use "git add <file>..." to update what will be committed)
  # (use "git checkout -- <file>..." to discard changes in working directory)
  #
  # modified: cgnat_cfg_tracker_comm.slax
  #

## Slide 42: Workflow – GIT – Diff – Changes file
  logut-mba13:dev logut$ git diff
  diff --git a/cgnat_cfg_tracker_comm.slax b/cgnat_cfg_tracker_comm.slax
  index 4d2fd31..2fbbbef 100644
  --- a/cgnat_cfg_tracker_comm.slax
  +++ b/cgnat_cfg_tracker_comm.slax
  @@ -1,7 +1,7 @@
  /*
  * Filename : cgnat_cfg_tracker_comm.slax
  * Author : Levent Ogut logut@juniper.net
  - * version : 1.4
  + * version : 1.5
  * Platform : MX
  * Release : Junos 11.4+
  *
  @@ -44,6 +44,7 @@ commit {
  1.2 fix of backup RE commit error.
  1.3 fix of private_prefix
  1.4 multiple input styles (low / high / prefix) can be accepted now
  +1.5 fix for public multiple format
  ### Sample Output
  <?xml version="1.0"?>
  @@ -195,7 +196,7 @@ match configuration {
  <high> $public_high;
  }
  if ($public_prefix != "") {
  - var $prefix = { call prefix2min_max ($address=$public_prefix); }
  + var $prefix := { call prefix2min_max ($address=$public_prefix); }
  <prefix> $public_prefix;
  <low> $prefix/min;
  <high> $prefix/max;
  @@ -410,7 +411,7 @@ template generate_filename () {
  /* first we find the new sequence number */
  var $rpc_file_list = <file-list> {
  - <path> $path _ $hostname _ "*";
  + <path> $path _ $hostname _ "*" _ "xml";
  }
  var $file_list = jcs:execute( $connection, $rpc_file_list );
  /* filename last will be presented as "/path/to/file/filename" e.g. /var/tmp/flint_20131211_000000_10.tmp */

## Slide 43: Workflow – GIT – Diff – between commits
  logut-mba13:automation_demo logut$ git diff 5f4f038d9dbf6a8704d7e58bc81778aa6e884aed 68a1b1529fda9e72e01817c1eb941f6ee23de2ae
  diff --git a/test.slax b/test.slax
  index e9e6ac3..8836a06 100644
  --- a/test.slax
  +++ b/test.slax
  @@ -1,2 +1 @@
  deneme
  -second line change
  logut-mba13:automation_demo logut$

## Slide 44: SourceTree Free Client for GIT sourcetreeapp.com

## Slide 45: Py-junos-eznc
  http://techwiki.juniper.net/Automation_Scripting/Junos_OS_PyEZ
  https://github.com/Juniper/py-junos-eznc
  http://techwiki.juniper.net/Automation_Scripting/Junos_OS_PyEZ/Hello%2C_World!

## Slide 46: Py-junos-eznc – Hello World Example
  logut@death> show configuration | find services
  services {
  ftp;
  ssh;
  telnet;
  xnm-clear-text;
  netconf {
  ssh;
  }
  }

## Slide 47: Py-junos-eznc – Hello World Example
  from pprint import pprint
  from jnpr.junos import Device
  my_junos_router = Device(host='death.jtac-emea.jnpr.net', user=’xxxxxx', password=’xxxxx' )
  my_junos_router.open()
  pprint( my_junos_router.facts )
  my_junos_router.close()

## Slide 48: Py-junos-eznc – Hello World Example
  logut-mba13:tmp logut$ python j.py
  {'2RE': True,
  'HOME': '/var/home/remote',
  'RE0': {'last_reboot_reason': 'Router rebooted after a normal shutdown.',
  'mastership_state': 'master',
  'model': 'RE-A-1000',
  'status': 'OK',
  'up_time': '7 days, 24 minutes, 55 seconds'},
  'domain': 'jtac-emea.jnpr.net',
  'fqdn': 'death.jtac-emea.jnpr.net',
  'hostname': 'death',
  'ifd_style': 'CLASSIC',
  'master': 'RE0',
  'model': 'M120',
  'personality': 'M',
  'serialnumber': 'JN109064CAEA',
  'switch_style': 'NONE',
  'version': '11.4R9-S1',
  'version_RE0': '11.4R9-S1',
  'version_info': junos.version_info(major=(11, 4), type=R, minor=9-S1, build=9-S1)}
  logut-mba13:tmp logut$

## Slide 49: Resources
  Script Hackers @ Matrix
  JUNOS as a Scripting Language On Demand Course
  This Week: Junos Automation Reference for SLAX 1.0
  This Week: Mastering Junos Automation
  This Week: Applying Junos Automation
  Navigating The Junos XML Hierarchy
  Docs @ Techpubs
  Junos OS Configuration and Operations Automation Guide
  Junos XML API Operational Reference
  Junos XML API Configuration Reference
  Junos XML Management Protocol Guide

## Slide 50: Resources Cont’d
  https://github.com/Juniper/juise
  https://github.com/Juniper/py-junos-eznc
  Sublime SLAX Plugin by David Gethings
  Vim SLAX Plugin
  JUNOScriptorium
  https://techwiki.juniper.net/Automation_Scripting
  https://www.juniper.net/us/en/community/junos/script-automation/library/configuration/
  https://www.juniper.net/us/en/community/junos/script-automation/library/event/
  https://www.juniper.net/us/en/community/junos/script-automation/library/operations/
  Subscribe to script-hackers at JAM

## Slide 51: New To scripting?
  Use all resource as above but also :
  Ask your manager to shadow a colleague for a scripting project
  Ask your manager to get a mentor/reviewer for your first few projects
  Do not forget you are never alone.

## Slide 52
Q&A
2014-02-20: LO
Notes: 52